Sum_Channels Block

1. Functionality

The block is used to maintain the history of symbols in a DSP system. It provides the sum of the last 4 or 8 valid values, coming to the block from 64 input channels. The sum goes to the output 5 clocks after data has arrived, including the latest valid data on data_in. The system also provides valid sum even if only one valid data item is received for a channel.

The input data is 8 bit wide and is treated as unsigned.

    Signals

Input signal	Width (bits)	Output signal	Width (bits)
valid_in	1	valid_out	1
data_in	8
chan_id_in	6	chan_id_out	6
host_data_in	8	host_data_out	8
host_addr	1
host_wr	1
host_rd	1
		sum_out	11
		ready	1

     Registers

Registers	Size(bits)	Description
mode	1	'0' = 4 last bytes summary. '1' = 8 last bytes summary.
mod	3	Constant used for fifo's write pointers.
v1_t0, v2_t1, v3_t2, v4_t3	4 x 1	Valid_in pipeline registers
d1_t0, d2_t1, d3_t2, d4_t3	4 x 8	Data_in pipeline registers
c1_t0, c2_t1, c3_t2, c4_t3, c5_t4, c6_t5	2 x 6	Channel_id_in pipeline registers
q1_t3	8	The last element in fifo
q2_t3	11	Current sum
wp0, wp1 ... wp63	64 x 3	Write pointers for the 64 channels
bp1, bp2	2 x 8	Bypass registers
wp	3	Write pointer
host	2 x 8	Host_data_in buffers
r0, r1	2 x 8	Host_data_in registers
hr_bf	8	Host_data_out delay register

        Memory

Name	Size(bits)	Description
History	512 x 8	History of valid data, holds 64 logical FIFOs
Accumulators	64 x 11	Current sums
Host Data Buffers	2 x 8	The latest values of host_data_in

2. Subsystems

The system is divided in four subsystems: Fifos, Sums, Host and Sum_block which all have common reset, clock and ready signals. Ready signal tells that we can receive valid data on the input starting from the next clock.

Sum_block is the core of the system and it controls both Fifos and Sums. Host is responsible for maintaining an additional protocol.

2.1. Fifos

Fifos is organized as memory of 512 x 8 cells, which are used as 64 logical FIFOs by the Sum_block.
2.2. Sums
Sums block contains a memory - 64 x 11 – where the sums are stored.
   2.3. Sum_block

Sum_block is all the logic which controls Fifos and Sums memories. It could be devided in subblocks.
+

1

wp=mod
0

0
mod

1
0

1

64

6

valid_in

wp
wpXX

channel_id_in

The action this logic block is doing is to provide the pointer for the channel and increment it. First the value of the register, which can be from wp0 to wp63, is incremented by one and then compared to mod value. If they are equal then wpXX register get zero value else incremented value. Not incremented value is sent trhrough a selecting logic wih 6 bit select which is channel and 64 3-bit registers as input.

-

8
11

1
0

1
0

+

1
0

0

sum_out
sums_in
bp1
bp1
bp2
q2_t3
d4_t3
v4_t3
q1_t3

con1
con2

First the right sum channel must be selected. Because it is impossible to store the sum and on the next cycle to get it from the memory, two bypass registers are used and two conditions are checked. Con1 is true when the channels on a current cycle and two cycles before are equal. Con2 is true when in two consecutive cycles the channels are equal. If con2 is true, then the temporary sum bp1 is used. If con1 is true then is used bp2. Then the last item in fifo is subtracted from the sum and the result is added to the current valid data. The new calculated sum is sent to the out if the data is valid, to the bypass register bp1 and is stored in sums memory.

When valid_in is asserted, the data on the data bus data_in is fetched to the first stage of a four-stage data_in pipeline, consisting of the registers d1_t0, d2_t1, d3_t2, d4_t3. This pipeline allows required five clocks delay between the valid data and the valid sum to be satisfied. There is a similar pipeline for valid_in signals which consists of v0_t0, v1_t1, v3_t2, v4_t3 registers. Also, a six-step pipeline is implemented for delay of channel_id_in signal from the input to the Sums. It provides the higher part of the address of the read and write pointers for both memories - Fifos and Sums – to arrive on the right clock.
There is one work 4-bit register – mod – which equals to 3 or 7, depending on the value of mode. It is used in the logic for calculating the next write pointer address.
Valid data, coming from data_in, is stored in the Fifos memory and is accessed via 64 3-bit write pointers (wp1, wp2, ..., wp64).
Channel_id_in is used in a 64-way multiplexer for selecting the appropriate write pointer wp0, wp1, ... wp64 to be accessed and incremented.
The 9-bit address of the FIFO memory is combined from the values of write pointer and channel_id_in. Selected write pointer is interpreted as 3 less significant bits of the address and the channel_id_in is used as 6 most significant bits of it.
The sum for each of the channels is updated on each valid data in the memory of Sums block. It is calculated by subtracting the last item in the channel's fifo from the current sum and adding the result to the incoming valid data.

 2.3. Host

1
0

1
0

1
0

1
0

0

1
0

1
0

r0
r1
host_data_in
host_wr
host_addr
host_rd

    When host_wr is asserted, the data on host_data_in is stored to the respective register – r0 or r1.
When host_rd is asserted, the value of the respective register is transferred to the delay register hr_bf. This allows data to be sent to host_data_out with two clocks delay after host_rd is asserted.

Designed by Krassimir and Todor, 2.2008
Training project